Easy Picking
System information

# System in use
## Overview
The system currently in use is called Easy Picking (hereinafter referred as EP) and it performs the following actions:
- Receive data from the Warehouse Management System (hereinafter referred as WMS)
  The interface used to exchange data between WMS and PCS is described in Appendix A
- Executes commands from the user
  The user’s manual is alleged to this document
- Control the process
  Returns the results of the process to the WMS
## Communication Interface
Data exchange between WMS and EP is made with a file-to-file method that uses a shared folder managed by a SMB protocol server and a FTP server on managed by the process control machine.
WMS  PCS
Name	Description	Transfer method
Products data list	File named articoli.txt	SMB
Products locations	File named mappa.txt	SMB
Customers’ orders data	File named ordini.txt	SMB
Dummy orders data (Amazon)	File named ordini_bertello.txt	SMB
Dummy orders packages data (Amazon)	File named colli_bertello.txt	SMB
Dummy orders items data (Amazon)	File named righe_bertello.txt	SMB
Delivery documents	PDF files printed by EP	FTP

PCS  WMS
Name	Description	Transfer method
Completed orders data	File named ordcni.txt	SMB
Completed packages data	File named colli.txt	SMB

## Warehouse plant
The warehouse is made of two main areas (isles).
Every isle is made of 8 sectors.
Every sector is composed by a a variable number of locations containing the products to pick and a display gathering information about the picking process.
On every location the is a light button controlled by the pick by light process.
## Warehouse equipment
### Process control server
The main control server executes all the logic of the warehouse. It’s a database server, a file exchange server, an application server and it can communicate with the PLC of the production line.
### IO Modules
The picking process and the packages handling is controlled by digital I/O signals
### Isle machines
Put in the beginning of each isle, used to gather information about the picking process and to execute some operative functions.
### Control station machine
This PC controls the weight of the packages. It is connected to a weighing device and two barcode readers, one for the weighing station and the other for the palletizer station.
### Laser printers
Used to print the delivery’s documents, network connected.
### Label printers
Used to print the delivery’s label, network connected.
## Workflow
### Packages filling
#### Packages formats
The system uses three packages’ formats – small – medium – large.
#### Filling algorithm
EP calculates the number of boxes and how to fill them given the packages dimensions, the products dimensions and weight.
##### Algorithm rules:
- The sequence of the picking process is defined by the sorting order of the picking locations.
- If an order row composed by more than one picking unit cannot be put all in one package it will be split in two or more rows and put in the next package.
- If an order row composed by one or more picking unit cannot be put all in one package and it can be split, it will be split in two or more rows and put in the next package.
- If an order row is related to a product that cannot stay horizontally but only vertically the algorithm will choose the right package by dimensions.
#### Sub orders by isle
Due to the topology of the production line the order is divided in two sub-orders by the isle in which the items are located.
#### Sub order by packages number
Each sub-order can be divided in more sub-orders to keep the number of the packages of each sub-order less or equal to 6.
After this calculation, the order is ready to be processed.
In the first sector of each isle the operator is instructed by the display on which package format to pick, a label is printed at the same time this information appears on the sector’s display as well as the shipping documents.
## Packages processing
After being picked and labelled and the alleged with the printed documents the package will proceed through the line to be filled with the products picked from the locations, this process is made by operators instructed by the information in the sector’s display and the lights on the location’s buttons.
The operator picks the product located where the light is on and press the related button so that the process can pass to the next product to pick. The quantity and all the information about the product are displayed in the sector’s display. When the picking list for the sector is completed, the package can pass to the next sector or, if the sector is the last of the isle, to the end of the production line, the control station.
### Packages control and destination
In the control station the barcode printed in the package’s label is read and the package’s weight is detected; if the system sees a difference between the theoretical weight and the detected one and this difference is more than a specific tolerance managed by the system, the package is pushed in a control zone, where the operator can check the contained products against the picking list contained in the system’s database for that package.
Otherwise, the package continue the journey to the palletizer where i twill be read by another barcode reader to control its destination based on information written in the system’s database.

# Data structure
Files containing data are ascii files, positional, fixed sizes, every row is terminated by line feed (0x0a)
In case the record has a record type it will be the first character of the record’s row.
### Data structure definition
#### Order header table
Filename : ordini.txt
Record type : T
Field Name	Field Type	Field Len	Description
ORDPROG	C	10	Order Number
RODSCLI	C	35	Customer Name
ROINCLI	C	35	Customer Address
ROLOCLI	C	35	Customer City
ROCPCLI	C	5	Customer ZIP code
ROTRNSP	C	2	Transit Point
ROTRATT	C	2	Secondary Trait
ROPRCLI	C	2	Customer Province
ROFLPAR	N	3	Bartolini Starting Branch
RODSPAR	C	35	Bartolini Starting Branch Description
ROTRMAR	N	3	Bartolini Arrival Terminal
ROFLARR	N	3	Bartolini Arrival Branch
RODSARR	C	35	Bartolini Arrival Branch Description
ROZNCON	N	2	Bartolini Delivery Zone Code
RONRSER	N	2	Serial Number
RONELAB	C	10	Elaboration Number
ROFLPRI	C	1	Priority Flag
ROFLAMZ	N	1	Amazon Flag
ROFLINC	N	1	Not complete order Flag

#### Order item table
Filename : ordini.txt
Record type : R
Field Name	Field Type	Field Len	Description
ORDPROG	C	10	Order Number
RACDPRO	C	18	Product code
RAQTORD	N	5	Quantity

Example (combined T/R)
T2416060678Spett. ARZILLI PAOLA VIA BERIGNANO 3 SAN GIMINANO 530371109SI093BRESCIA 028080SIENA 68022000018656
R24160606781922454 00001
R241606067881099101 00001
R241606067881099114 00001
R241606067881099123 00001
R241606067881099125 00001
R24160606781856244 00001
R24160606781856271 00001
R24160606781875052 00003
R24160606781920652 00001
R24160606781920653 00001
R24160606781922350 00001
R24160606781922351 00001
R24160606781922451 00001
R24160606781922453 00001
R241606067881098103 00003
R241606067881099115 00001
R241606067881099118 00001
R241606067881099120 00001
R241606067881099122 00001
R241606067881099147 00001
R241606067881099148 00001
R241606067881099149 00001
R241606067890199007 00001

#### Product data table
Filename : articoli.txt
Field Name	Field Type	Field Len	Description
PRCDPRO	C	18	Product code
PRDESCR	C	40	Product Decription
PRLUNGH	N	3	Length mm
PRLARGH	N	3	Width mm
PRALTEZ	N	3	Height mm
PRSWALT	C	1	Product Standing Constraint (1:yes)
PRPESGR	N	5	Weight gr
PRQTPRS	N	2	Units per pick
PRVOLUM	N	6	Product volume in cc
PRCANCE	C	1	Deletion flag
PRPERIC	N	1	Dangerous good flag

example
81385396 KADUS POMPA PER FLACONE 1 L 280070070 0009201001372-0
81385483 SP_balance scalp pump 1L shampoo 300080080 0013401001920-0
81385519 WPC POMPA per flacone da 1000 ML 270060060 0009301000972-0
81385524 WPC POMPA per vaso da 500 ML 180110110 0005801002178-0

#### Location data
Filename : mappa.txt
Field Name	Field Type	Field Len	Description
UBICAZIONE	C	7	Product location
CODPROD	C	18	Product code
CANCELLA	C	1	Deletion Flag – Not used
LOCAZIONE	C	10	Decoded location – Not used

example
104104181136412 0000000000
104206181385519 0000000000
108107181385524 0000000000

#### Dummy order data
Filename : ordini_bertello.txt
Field Name	Field Type	Field Len	Description
ORDPROG	C	10	Order Number
OPNMCLL	N	6	Number of Boxes
RONMRGH	N	6	Number of Rows
RONMCPE	N	6	Number of Items
ROPSPRE	N	6	Calculated Weight

example
30157509500000010000080000660078002000056261
#### Dummy order packages data
Filename : colli_bertello.txt
Field Name	Field Type	Field Len	Description
ORDPROG	C	10	Order Number
CPNMCOL	N	6	Box Number
CPNMRGH	N	6	Number of Rows
CPNMCPE	N	6	Number of Items
CPPSPRE	N	6	Calculated Weight
CPTPFOR	C	18	Box type (H0001-H0002-H0003)

example
3015750950000001000008000066007800
#### Dummy order items data
Filename : righe_bertello.txt
Field Name	Field Type	Field Len	Description
ORDPROG	C	10	Order Number
RPNMCOL	N	6	Box Number
RPCDPRO	C	18	Product Code
RPCDEAN	C	13	EAN Product Code
RPNMCPE	N	6	Number of items
RPPESGR	N	6	Weight of the row

example
3015750950000001000000022001014002007800000006000390
3015750950000001000000022001014047007800000006000390
3015750950000001000000022001014082007800000006000390
3015750950000001000000022001014087007800000024001560
3015750950000001000000022001014109007800000006000390
3015750950000001000000022001014124007800000006003900
3015750950000001000000022001014166007800000006000390
3015750950000001000000022002387011007800000006000390
#### Data return - orders
Filename : ordcni.txt
Field Name	Field Type	Field Len	Description
ORDPROG	C	10	Order Number
RONMCOL	N	3	Number of Boxes
ROPSREA	N	6	Total Weight gr
RONELAB	N	10	Elaboration Number

example
3016392628 4 393382000056640
3016393284 1 15232000056640
#### Data return - packages
Filename : col_cni.txt
Field Name	Field Type	Field Len	Description
ORDPROG	C	10	Order Number
CPTPFOR	C	18	Box type (H0001-H0002-H0003)
CPPRGCL	N	7	Pack code

example
3016392628H0003 1131235
3016392628H0003 1131236
3016392628H0003 1131237
3016392628H0003 1131238
3016393284H0002 1131239
# File transfer
Data files are located in a specific path in the PBL machine
This path is accessible via SMB protocol (samba) and FTP.
In the main folder (root) are located all the files described above.
In the (root)/pdf are located the pdf documents related to the order to be processed.
The PDF documents filenames are 15 chars long and start with a letter defining the document type:

F	Fattura (Invoice)
D	DDT (transport document)
N	No document

Followed by 10 chars related to the order ID.

Example of pdf document filename related to order ID 0123456789
F0123456789.pdf

FTP access data:
IP: 172.28.194.11
user: picking
password: picking
main folder: /u/prj/wella/export_sap